## Slide 1
Introduction

## Slide 2: Course Information
Course materials on Unilica (enrollment key: JTMOH)
  Make sure you update your notification settings to receive messages.
Instructors:
  Alper Sarıkan (1-2)
  Satılmış Topcu (3-4)
  Mustafa Ozdal (5-6)
Grading:
  Quizzes: 15%
  Labs: 15%
  Project: 10%
  Midterm exam: 30%
  Final exam: 30%
You should buy BASYS3 board for labs and project

## Slide 3: Course Information
FZ POLICY: Students who fail to meet the following requirements will receive a grade of FZ:
1. Weighted average score of the midterm exam and quizzes ≥ 40%
(2 x midterm_score + avg_quiz_scores)/3 ≥ 40%
2. Average score of the labs and project ≥ 50%
(avg_lab_score + project_score)/2 ≥ 50%
3. Absent from no more than 1 lab
  Only the grades until the FZ deadline will be considered while computing the average scores above. Students who receive FZ cannot attend the final exam.

## Slide 4: Course Information
TEXTBOOK: David Money Harris, Sarah L. Harris, Digital Design and Computer Architecture, 2nd ed. Morgan Kaufmann, 2013.
Exams will be open book. Only original and unmarked textbooks will be allowed in the exams. If you have any notes/drawings/markings/etc. on your textbook, you will not be able to use it in the exams.
RECOMMENDED BOOK: Frank Vahid, Digital Design, with RTL Design, VHDL and Verilog, 2nd ed. John Wiley, 2011.

## Slide 5: Why Study Hardware?
Career in hardware design
  Numerous new hardware devices introduced these days: Smartphones, smart homes, wearables, internet of things, drones, VR glasses, …
Good software programmers know about hardware
  Anyone can write a web/smartphone app!
  Inherent knowledge of computers needed to program efficiently

## Slide 6: Software & Hardware Co-Design

## Slide 7
Digital Design and Computer Architecture, 2nd Edition
Chapter 1
David Money Harris and Sarah L. Harris

## Slide 8
Background
The Game Plan
The Art of Managing Complexity
The Digital Abstraction
Number Systems
Logic Gates
Logic Levels
CMOS Transistors
Power Consumption
Chapter 1 :: Topics

## Slide 9
Purpose of course:
  Understand what’s under the hood of a computer
  Learn the principles of digital design
  Learn to systematically debug increasingly complex designs
  Design and build a microprocessor
The Game Plan

## Slide 10
Abstraction
Discipline
The Three –Y’s
  Hierarchy
  Modularity
  Regularity
The Art of Managing Complexity

## Slide 11
Hiding details when they aren’t important
Abstraction

## Slide 12
Intentionally restrict design choices
Example: Digital discipline
  Discrete voltages instead of continuous
  Simpler to design than analog circuits – can build more sophisticated systems
  Digital systems replacing analog predecessors:
    i.e., digital cameras, digital television, cell phones, CDs
Discipline

## Slide 13
Most physical variables are continuous
  Voltage on a wire
  Frequency of an oscillation
  Position of a mass
Digital abstraction considers discrete subset of values
The Digital Abstraction

## Slide 14
Two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0: voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels to represent 1 and 0
Bit: Binary digit
Digital Discipline: Binary Values

## Slide 15
Hierarchy
  A system divided into modules and submodules
Modularity
  Having well-defined functions and interfaces
Regularity
  Encouraging uniformity, so modules can be easily reused
The Three -Y’s

## Slide 16
Source: https://www.prlog.org/10792126-mems-sensors-for-smartphones-report.html

## Slide 17
Decimal numbers
Binary numbers
Number Systems

## Slide 18
Decimal numbers
Binary numbers
Number Systems

## Slide 19
20 =
21 =
22 =
23 =
24 =
25 =
26 =
27 =
28 =
29 =
210 =
211 =
212 =
213 =
214 =
215 =
Powers of Two

## Slide 20
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
Handy to memorize up to 29
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two

## Slide 21
Binary to decimal conversion:
  Convert 100112 to decimal
Decimal to binary conversion:
  Convert 4710 to binary
Number Conversion

## Slide 22
Decimal to binary conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 23
N-digit decimal number
  How many values?
  Range?
  Example: 3-digit decimal number:
N-bit binary number
  How many values?
  Range:
  Example: 3-digit binary number:
Binary Values and Range

## Slide 24
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 25
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 
1 | 1 | 
2 | 2 | 
3 | 3 | 
4 | 4 | 
5 | 5 | 
6 | 6 | 
7 | 7 | 
8 | 8 | 
9 | 9 | 
A | 10 | 
B | 11 | 
C | 12 | 
D | 13 | 
E | 14 | 
F | 15 | 
Hexadecimal Numbers

## Slide 26
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111
Hexadecimal Numbers

## Slide 27
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 28
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
Hexadecimal to decimal conversion:
  Convert 0x4AF to decimal
Hexadecimal to Binary Conversion

## Slide 29
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 30
Bits
Bytes & Nibbles
Bytes
Bits, Bytes, Nibbles…

## Slide 31
210 = 1 kilo ≈ 1000 (1024)
220 =
230 =
Large Powers of Two

## Slide 32
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
Large Powers of Two

## Slide 33
What is the value of 224?
How many values can a 32-bit variable represent?
Estimating Powers of Two

## Slide 34
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 35
Decimal
Binary
Addition

## Slide 36
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 37
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Overflow!
Binary Addition Examples

## Slide 38
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 39: Exercise 1.66
A flying saucer crashes in a Nebraska cornfield. The FBI investigates the wreckage and finds an engineering manual containing an equation in the Martian number system: 325+42 = 411. If this equation is correct, how many fingers would you expect Martians to have?

## Slide 40
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 41
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 =
- 6 =
Range of an N-bit sign/magnitude number:
Sign/Magnitude Numbers

## Slide 42
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 43
Problems:
  Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
  Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 44
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
  Most Significant bit is the sign bit 0 if positive 1 if negative
  For a binary number A
  If A>0 or A=0 then two’s complement representation of A is A (no change)
  If A< 0 then two’s complement of A is 2n-A
  Example
  A=-6 +6=0110
  24 – 0110= 10000-0110 = 1010=-6
Two’s Complement Numbers

## Slide 45
Msb has value of -2N-1
Most positive 4-bit number:
Most negative 4-bit number:
The most significant bit still indicates the sign (1 = negative, 0 = positive)
Range of an N-bit two’s comp number:
Two’s Complement Numbers

## Slide 46
Msb has value of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s comp number:
  [-(2N-1), 2N-1-1]
Two’s Complement Numbers

## Slide 47
Flip the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
“Taking the Two’s Complement”

## Slide 48
Flip the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
“Taking the Two’s Complement”

## Slide 49
Take the two’s complement of 610 = 01102
What is the decimal value of 10012?
Two’s Complement Examples

## Slide 50
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 51: True or False
I can take 2s complement of a number as follows:
  Examine the bits starting from the LSB
  Let k be the index where the first “1” is found
  Invert all bits to the left of k

## Slide 52
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 53
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 54
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 55
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 56
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 00112 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 57
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 58
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 59
Single-Input Logic Gates

## Slide 60
Single-Input Logic Gates

## Slide 61
Two-Input Logic Gates

## Slide 62
Two-Input Logic Gates

## Slide 63
More Two-Input Logic Gates

## Slide 64
More Two-Input Logic Gates

## Slide 65
Multiple-Input Logic Gates

## Slide 66
Multi-input XOR: Odd parity
Multiple-Input Logic Gates

## Slide 67: Questions
How many unique 2-input logic functions can we define?
How many unique k-input logic functions can we define?

## Slide 68
Discrete voltages represent 1 and 0
For example:
  0 = ground (GND) or 0 volts
  1 = VDD or 5 volts
What about 4.99 volts? Is that a 0 or a 1?
What about 3.2 volts?
Logic Levels

## Slide 69
Range of voltages for 1 and 0
Different ranges for inputs and outputs to allow for noise
Logic Levels

## Slide 70
What is Noise?

## Slide 71
Anything that degrades the signal
  E.g., resistance, power supply noise, coupling to neighboring wires, etc.
Example: a gate (driver) outputs 5 V but, because of resistance in a long wire, receiver gets 4.5 V
What is Noise?

## Slide 72
With logically valid inputs, every circuit element must produce logically valid outputs
Use limited ranges of voltages to represent discrete values
The Static Discipline

## Slide 73
Logic Levels

## Slide 74
NMH = VOH – VIH
NML = VIL – VOL
Noise Margins

## Slide 75: Exercise

## Slide 76
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
Be careful connecting chips with different supply voltages
Chips operate because they contain magic smoke
Proof:
  if the magic smoke is let out, the chip stops working
VDD Scaling

## Slide 77
Logic Family | VDD | VIL | VIH | VOL | VOH
TTL | 5 (4.75 - 5.25) | 0.8 | 2.0 | 0.4 | 2.4
CMOS | 5 (4.5 - 6) | 1.35 | 3.15 | 0.33 | 3.84
LVTTL | 3.3 (3 - 3.6) | 0.8 | 2.0 | 0.4 | 2.4
LVCMOS | 3.3 (3 - 3.6) | 0.9 | 1.8 | 0.36 | 2.7
Logic Family Examples

## Slide 78
Logic gates built from transistors
3-ported voltage-controlled switch
  2 ports connected depending on voltage of 3rd
  d and s are connected (ON) when g is 1
Transistors

## Slide 79
Nicknamed “Mayor of Silicon Valley”
Cofounded Fairchild Semiconductor in 1957
Cofounded Intel in 1968
Co-invented the integrated circuit
Robert Noyce, 1927-1990

## Slide 80
Transistors built from silicon, a semiconductor
Pure silicon is a poor conductor (no free charges)
Doped silicon is a good conductor (free charges)
  n-type (free negative charges, electrons)
  p-type (free positive charges, holes)
Silicon

## Slide 81
Metal oxide silicon (MOS) transistors:
  Polysilicon (used to be metal) gate
  Oxide (silicon dioxide) insulator
  Doped silicon
MOS Transistors

## Slide 82
Gate = 0
OFF (no connection between source and drain)
Gate = 1
ON (channel between source and drain)
Transistors: nMOS

## Slide 83
pMOS transistor is opposite
  ON when Gate = 0
  OFF when Gate = 1
Transistors: pMOS

## Slide 84
Transistor Function

## Slide 85
nMOS: pass good 0’s, so connect source to GND
pMOS: pass good 1’s, so connect source to VDD
Transistor Function

## Slide 86
A | P1 | N1 | Y
0 |  |  | 
1 |  |  | 
CMOS Gates: NOT Gate

## Slide 87
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0
CMOS Gates: NOT Gate

## Slide 88: What is the function of this gate?

## Slide 89
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 |  |  |  |  | 
0 | 1 |  |  |  |  | 
1 | 0 |  |  |  |  | 
1 | 1 |  |  |  |  | 
CMOS Gates: NAND Gate

## Slide 90
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
CMOS Gates: NAND Gate

## Slide 91
CMOS Gate Structure

## Slide 92
How do you build a three-input NOR gate?
NOR Gate

## Slide 93
NOR3 Gate

## Slide 94
How do you build a two-input AND gate?
Other CMOS Gates

## Slide 95
AND2 Gate

## Slide 96: What is the function of this gate?

## Slide 97: What is the function of this gate?

## Slide 98
Cofounded Intel in 1968 with Robert Noyce.
Moore’s Law: number of transistors on a computer chip doubles every year (observed in 1965)
Since 1975, transistor counts have doubled every two years.
Gordon Moore, 1929-

## Slide 99
“If the automobile had followed the same development cycle as the computer, a Rolls-Royce would today cost $100, get one million miles to the gallon, and explode once a year . . .”
– Robert Cringley
Moore’s Law

## Slide 100
Power = Energy consumed per unit time
  Dynamic power consumption
  Static power consumption
Power Consumption

## Slide 101
Power to charge transistor gate capacitances
  Energy required to charge a capacitance, C, to VDD is CVDD2
  Circuit running at frequency f: transistors switch (from 1 to 0 or vice versa) at that frequency
  Capacitor is charged f/2 times per second (discharging from 1 to 0 is free)
Dynamic power consumption:
Pdynamic = ½CVDD2f
Dynamic Power Consumption

## Slide 102
Power consumed when no gates are switching
Caused by the quiescent supply current, IDD (also called the leakage current)
Static power consumption:
Pstatic = IDDVDD
Static Power Consumption

## Slide 103
Estimate the power consumption of a wireless handheld computer
  VDD = 1.2 V
  C = 20 nF
  f = 1 GHz
  IDD = 20 mA
Power Consumption Example

## Slide 104
Estimate the power consumption of a wireless handheld computer
  VDD = 1.2 V
  C = 20 nF
  f = 1 GHz
  IDD = 20 mA
P = ½CVDD2f + IDDVDD
= ½(20 nF)(1.2 V)2(1 GHz) +
(20 mA)(1.2 V)
= 14.4 W
Power Consumption Example